## Slide 1
BANK ENTERPRISE NETWORK MODEL
Page | 01
ON CISCO PACKET TRACER

## Slide 2
PROJECT
This project, titled "Bank Enterprise Network on Cisco Packet Tracer," is developed as a semester project for the Data Communication and Networking (DCN) course. The network is designed to simulate a large-scale banking environment and includes connectivity and communication between 12 distinct departments, each representing a functional unit within a real-world banking organization.
To ensure efficient data forwarding and network scalability, dynamic routing protocols have been configured to interconnect all departmental networks. These protocols enable automatic route recalculation in response to topology changes, ensuring optimal path selection, improved convergence, and streamlined network management.
INTRODUCTION

## Slide 4
I
www.reallygreatsite.com
Page | 05
BANK ENTERPRISE – FLOOR-WISE DEPARTMENT DISTRIBUTION
01
Floor 1:
  Account Services / Retail Banking
  Customer Service / Teller Department
  Marketing and Sales
02
03
04
The bank enterprise is structured across 4 floors, with 3 departments on each floor, simulating a multi-layered enterprise network topology.
Floor 2:
  Human Resources (HR)
  Foreign Exchange / International Banking
  Finance
Floor 3:
  Risk Operations (ROP) and Legal Compliance
  IT and Network Administration
  [One slot left blank if needed, or noted as reserved]
Floor 4:
  Security Department
  Server Room
  Cybersecurity Operations Center (CSOC)

## Slide 5
Page | 07
🛰️ SMART IP ALLOCATION STRATEGY ACROSS BANK DEPARTMENTS
To ensure structured communication across the bank enterprise network, 12 separate networks have been designed — each assigned to a specific department.
  Each network is based on a /24 subnet (e.g., 192.1.X.0/24), allowing up to 254 usable host IPs per department.
  A unique Network Address, Default Gateway, and IP Range is assigned to each department to maintain logical segmentation.
  Default Gateway (e.g., 192.1.1.1) is configured on Layer 3 devices to enable inter-VLAN routing and external communication.
  The usable IP range starts from .2 to .254, with a reserved starting IP for hosts (e.g., .12) to maintain consistency in configuration.
  This structured IP plan improves network manageability, troubleshooting, and scalability.

## Slide 6
Page | 03
FLOOR 1 NETWORK OVERVIEW
  Hosts the following departments:
    Account Services
    Customer Service / Teller Department
    Marketing and Sales
  Each department includes:
    LAN-connected PCs and network printers
    Connected through a Layer 2 switch for intra-department communication
  All devices receive IP addresses via DHCP,
    DHCP server is located on Floor 4 (Server Room)
  Server Access:
    Customer Service and Marketing departments host local departmental database servers
    Account Services accesses the main centralized database server
  Credential-based authentication is required for all users to access servers and shared resources
  Assigned subnets:
    192.1.1.0/24 – Account Services
    192.1.2.0/24 – Customer Service
    192.1.3.0/24 – Marketing and Sales
  Dynamic routing enables secure and efficient inter-department communication across the enterprise network

## Slide 7
Page | 03
FLOOR 2 NETWORK OVERVIEW
  Hosts the following departments:
    Human Resources (HR)
    Finance
    Foreign Exchange / International Banking
  Each department includes:
    LAN-connected PCs and network printers
    Connected through a Layer 2 switch for intra-department communication
  All devices receive IP addresses via DHCP,
    DHCP service is provided by the central DHCP server on Floor 4 (Server Room)
  Server Access:
    All departments access the main centralized database server hosted in the Server Room on Floor 4
  Credential-based authentication is enforced for secure access to shared resources and database systems
  Assigned subnets:
    192.1.4.0/24 – Human Resources
    192.1.5.0/24 – Finance
    192.1.6.0/24 – Foreign Exchange / International Banking
  Dynamic routing protocols are used to ensure efficient inter-departmental and enterprise-wide connectivity

## Slide 8
Page | 03
FLOOR 3 NETWORK OVERVIEW
  Hosts the following departments:
    ROP and Legal Compliance
    IT and Network Administration
  Each department includes:
    LAN-connected PCs and network printers
    Connected through a Layer 2 switch for intra-department communication
  All devices receive IP addresses via DHCP,
    DHCP service is provided by the central DHCP server located on Floor 4 (Server Room)
  Server Access:
    The ROP and Legal Compliance department hosts its own dedicated departmental server
    IT and Network Administration departments manage and access core infrastructure services
  Credential-based authentication is enforced to ensure secure access to systems and data
  Assigned subnets:
    192.1.7.0/24 – Reserved for additional or future use
    192.1.8.0/24 – ROP and Legal Compliance
    192.1.9.0/24 – IT Department
  Dynamic routing protocols ensure efficient, scalable, and fault-tolerant communication across the enterprise network

## Slide 9
Page | 03
FLOOR 4 NETWORK OVERVIEW
  Hosts the following critical areas:
    Security Department
    Server Room
    Cybersecurity Operations Center (CSOC)
  Each area includes:
    LAN-connected workstations, monitoring systems, and secured servers
    Connected through Layer 2 switches with strict access control policies
  Server Room:
    Houses the central DHCP server that assigns IPs to all client devices across the enterprise
    Hosts centralized database servers, application servers, and backup systems
  Static IP addressing is used for all devices on this floor to enhance network control and security
  CSOC:
    Has complete monitoring and administrative access to all departmental servers across all floors
    Manages network security, threat detection, and incident response
  Assigned subnets:
    192.1.10.0/24 – CSOC
    192.1.11.0/24 – Server Room
    192.1.12.0/24 – Security Department
  Recognized as the most secured floor of the enterprise network due to its centralized infrastructure, restricted access, and critical role in cybersecurity operations